## Slide 1: Raspberry Pi 4 – wiringPi and Python 개발 설명서
정도윤(rabbit.white@daum.net)

## Slide 2: 목차
1. 작업 환경
2. 최신버전 WiringPi 설치하기
3. WiringPi – GPIO version 확인
4. WiringPi – GPIO readall
5. WiringPi – GPIO read
6. WiringPi – GPIO mode
7. WiringPi – GPIO write
8. WiringPi vs Thonny Python
9. WiringPi – (예제1)
10. WiringPi – (예제2)
11. WiringPi 컴파일 및 실행 방법
12. Thonny Python – (예제1: LED 깜박거리기)

## Slide 3: 1. 작업 환경
OS: RaspberryPi 4B Bullseyes(2022-05)

## Slide 4: 2. 최신버전 WiringPi 설치하기
sudo apt purge wiringpi
hash -r
git clone https://github.com/WiringPi/WiringPi.git
ls
cd WiringPi
git pull origin
./build
최신버전 WiringPi 설치하기

## Slide 5: 3. WiringPi – GPIO version 확인
gpio -v
GPIO version 확인

## Slide 6: 4. WiringPi – GPIO readall
gpio readall
GPIO readall
Readall 명령을 이용하여 pin에 대한 정보를 볼 수 있음.

## Slide 7: 4. WiringPi – GPIO readall
GPIO readall
라즈베리 핀을 이용할 때, BCM, wPi번호를 이용할 수 있음.
그리고 Mode는 입력이나 출력이냐 정보 V는 값이 HIGH(1), LOW(0)입니다.
예) wPi가 1번, 물리 핀 번호(Physical) 12번, BCM 18번 입니다.

## Slide 8: 5. WiringPi – GPIO read
GPIO read [번호]
현재 포트의 값을 읽을 수 있음.
gpio read 1

## Slide 9: 6. WiringPi – GPIO mode
GPIO mode [pin] [in/out/clock]
현재 포트의 모드를 설정할 수 있음.
gpio mode 1 out을 통해
wPi 1번의 mode가 In에서 Out으로 변경되었음.
gpio mode 1 out

## Slide 10: 7. WiringPi – GPIO write
GPIO write [pin] [1/0]
지정한 포트에 값을 쓸 수 있음.
gpio write 1 1

## Slide 11: 8. WiringPi vs Thonny Python
WiringPi
Thonny Python

## Slide 12: 9. WiringPi – (예제1)
1. WiringPi(C언어) - 1
#include <stdio.h>
#include <wiringPi.h>
#define LED 1
#define SWITCH 4
int main(){
if( wiringPiSetup() == -1)
return -1;
pinMode(LED, OUTPUT);
pinMode(SWITCH, INPUT);
while(1){
if ( digitalRead(SWITCH) == HIGH ){
printf("Button was pressed\n");
digitalWrite(LED, HIGH);
}
else{
printf("Button was NOT pressed\n");
digitalWrite(LED, LOW);
}
delay(1000);
}
return 0;
}

## Slide 13: 10. WiringPi – (예제2)
2. WiringPi(C언어) - 2
#include <stdio.h>
#include <wiringPi.h>
#define LED 1
#define SWITCH 4
int main(){
if( wiringPiSetup() == -1)
return -1;
pinMode(LED, OUTPUT);
pinMode(SWITCH, INPUT);
while(1){
digitalWrite(LED, HIGH);
delay(1000);
digitalWrite(LED, LOW);
delay(1000);
}
return 0;
}

## Slide 14: 11. WiringPi 컴파일 및 실행 방법
위에 작성한 코드를 실행하기 위해서는 컴파일을 해야 함.
gcc –o led led.c –lwiringPi
./led
[참고사항]
대소문자 주의할 것

## Slide 15: 12. Thonny Python – (예제1: LED 깜박거리기)
3. Thonny Python
import RPi.GPIO as GPIO
import time
def led(pin, t):
while(True):
GPIO.setmode(GPIO.BCM)
GPIO.setup(pin, GPIO.OUT)
GPIO.output(pin, True)
time.sleep(t)
GPIO.output(pin, False)
time.sleep(t)
print("hangul")
GPIO.cleanup(pin)
led(5, 3)